## Slide 1
Agentic AI for Drilling Operational Intelligence
SPE GCS 2026 ML Challenge Analyzing the Equinor Volve Field Dataset
Rong Lu | March 2026

## Slide 2
The Challenge
Build an evidence-based AI agent for drilling operational intelligence
Analyze the Equinor Volve Field drilling dataset
Answer 6 categories of operational questions:
  1. Drilling Phase Identification
  2. Time & Efficiency Analysis (NPT)
  3. Section & ROP Performance
  4. BHA Configuration Effectiveness
  5. Operational Issues & Root Causes
  6. Synthesis & Recommendations
Evaluation Criteria
Quality of REASONING (most important)
Evidence from BOTH data AND reports
Consistency across answers
Clear assumptions & uncertainty handling
Transparency & reproducibility
"Complexity alone will not be rewarded"

## Slide 3
System Architecture
Pure OpenAI SDK + DuckDB + ChromaDB | No LangChain, no framework bloat
User Question
  --> GPT-5.4 mini (tool calling, max 10 rounds)
  --> 12 Agent Tools (see right)
  --> Structured Answer with Evidence
Key features:
  Evidence Trace mode (--trace) shows every
  tool call, args, timing, and data sources
  Retry with exponential backoff for API resilience
  Output validation: checks all 6 required sections
12 Agent Tools
query_drilling_data SQL on 12 DuckDB tables
search_daily_reports Semantic search (ChromaDB)
get_well_overview Well metadata & formations
get_drilling_phases Hole-size + activity-code phases
compute_efficiency NPT sub-classification, ROP
compare_wells Side-by-side + production data
get_bha_configurations WITSML BHA + mudlog params
identify_issues Root cause + mud correlation
get_formation_context Geological depth context
get_field_benchmarks Cross-well rankings (5 modes)
get_ddr_narrative Guaranteed DDR text by date
generate_depth_time_plot Depth-vs-time visualization

## Slide 4
Data Integration
12 DuckDB tables from 4 data sources | Ingestion: ~3 minutes
1,759
DDR XML Files (zero parse errors)
23,447
Activity Records
2,882
MudLog Intervals (ROP/WOB/RPM/lithology)
11,134
WITSML Messages
~38K
ChromaDB Docs (DDR + WITSML)
DDR Daily Drilling Reports (core NLP source)
  23,447 activities with timestamps & codes
  2,271 fluid records (mud type, density, PV, YP)
  1,726 directional survey stations
  26,965 text documents (summaries + comments)
WITSML Real-Time Data (measured drilling parameters)
  2,882 mudlog intervals: actual ROP, WOB, torque, RPM
  161 official BHA runs across 14 wells
  4,217 trajectory stations (MD, TVD, incl, azi, DLS)
Production Data
  15,634 daily records: oil, gas, water, pressure
  7 wells: F-1C, F-11, F-12, F-14, F-15D, F-4, F-5
Geological Data
  409 formation tops across 26 wells
  48 perforation interval records
Data Quality
  Sentinel values (-999.xx) filtered at parse time
  Outlier filtering: RPM<=300, WOB<=500kN, ROP<=200 m/hr
  Unit conversions: m/s->m/hr, N->kN, rad->deg, kg/m3->sg

## Slide 5
Evidence-First Design
Every answer cites BOTH structured data AND daily report quotes
Mandatory Answer Structure (6 Sections)
1. Answer (clear, concise conclusion)
2. Evidence from Drilling Data (specific measurements)
3. Evidence from Daily Reports (DDR quotes with dates)
4. Reasoning (numbered step-by-step chain)
5. Assumptions (explicitly stated)
6. Confidence & Uncertainty (HIGH / MEDIUM / LOW)
Key Differentiators
WITSML mudlog = actual measured ROP/WOB/RPM
  (not estimated from daily depth progress)
Hole-size transitions define phases
  (not just generic activity code classification)
Formation context links ROP to geology
  (why is this section slow? check the lithology)
Statistical mud-problem correlation
  (problem-day vs normal-day property comparison)
NPT sub-classified by comment analysis
  (11 categories instead of generic 'Other NPT')

## Slide 6
Example: Phase Identification
Q: "Identify the major drilling phases for well 15/9-F-11 T2"
Agent Tool Calls
1. get_drilling_phases('15_9_F_11_T2')
2. get_ddr_narrative(well, date_from, date_to)
3. get_formation_context('15_9_F_11_T2')
Answer (3 major hole sections identified)
Phase 1: Surface 26" (Mar 24 - Apr 13)
  306m - 1,365m MD | avg ROP 41.6 m/hr
Phase 2: Intermediate 17.5" (Apr 14 - Apr 28)
  1,400m - 2,577m MD | avg ROP 29.2 m/hr
Phase 3: Reservoir 8.5" (Apr 29 - May 9)
  2,907m - 4,562m MD | avg ROP 19.0 m/hr
Evidence from Daily Reports
DDR 2013-04-14: "Drilled 17 1/2" hole from
  1368m to 1400m with 3675 l/min, 188 bar,
  60-140 RPM, 7-15 kNm, WOB 5 Ton"
DDR 2013-04-22: "Drilled 17 1/2" hole to
  section TD at 2574m. POOH and L/O
  17 1/2" steerable BHA."
Confidence: HIGH
  Hole size changes confirmed by activity
  codes, depth progression, and DDR summaries

## Slide 7
Cross-Well Analysis
Field-wide benchmarking across 26 wellbore sections
get_field_benchmarks (5 Modes)
daily_progress
  Ranks well-sections by avg drilled m/day
section_performance
  Difficulty index from WOB, torque, ROP z-scores
gas_response
  Peak methane/ethane in target formation window
risk
  Composite score: stuck/loss/kick mentions + severity
production_summary
  Cumulative oil/gas/water with normalized well names
Example Results
Hardest section to drill (by difficulty index):
  F-11 B 12.25" section (difficulty 3.07)
  avg ROP 25.0 m/hr | WOB 112.1 kN
Highest gas response in Hugin Fm:
  F-1 C: max CH4 35,013 ppm at 3229-4004m MD
Highest risk well:
  F-15: risk score 168.5 (51 severe mentions)
Top oil producer:
  F-12: cum oil 4.58M Sm3 over 3,056 prod days

## Slide 8
Evidence Trace: Transparent Reasoning
python -m src.main ask '...' --trace | Turns the black box into a glass box
## Evidence Trace
### Step 1: get_bha_configurations(well='15_9_F_11_T2')
  Retrieved: 3,475 chars | Duration: 0.26s
  Summary: 12 official BHA runs, ROP by section, lithology...
### Step 2: get_ddr_narrative(well='15_9_F_11_T2', date_from='2013-04-11', date_to='2013-04-26')
  Retrieved: 7,134 chars | Duration: 0.02s
  Summary: 16 DDR reports, 67 activities; "Drilled 17 1/2" hole to section TD..."
Total tool calls: 3 | Total evidence retrieval time: 0.29s
Data sources used: ddr_activities, ddr_status, witsml_bha_runs, witsml_mudlog
Judges can see EXACTLY how the agent reasoned. Maximum transparency.

## Slide 9
Key Design Decisions
"Complexity alone will not be rewarded" -- Judges
OpenAI SDK over LangChain
  Transparent, debuggable, minimal dependencies
DuckDB over SQLite / Postgres
  In-process analytical SQL, zero config, fast
ChromaDB for semantic retrieval
  Lightweight, embedded, cosine similarity
GPT-5.4 mini with reasoning_effort=high
  Best reasoning quality for drilling domain
  Graceful fallback for older models
Rule-based + LLM hybrid for phase detection
  Rules: hole sizes + activity codes (deterministic)
  LLM: validates against DDR narratives
Domain-specific tooling over generic agents
  Each tool purpose-built for a question category
  Tools return structured evidence, not raw data
Quality assurance
  95 automated tests, 130 stress-test questions
  Output validation checks all 6 answer sections
  Data quality filtering at ingestion + query time

## Slide 10
Why This Solution Wins
12 DuckDB tables from 4 data sources (DDR + WITSML + production + geology)
12 purpose-built agent tools covering all 6 question categories + cross-well benchmarks
~38,000 searchable documents in ChromaDB vector store (DDR text + WITSML messages)
Evidence-first: every answer cites BOTH data AND daily report quotes
Transparent: --trace shows complete reasoning chain for every answer
Domain-appropriate: hole-size phase detection, NPT sub-classification, mud correlation
Deep data integration: actual measured ROP/WOB/RPM from WITSML mudlog
Cross-well analysis: field-wide benchmarks, difficulty indices, gas response ranking
Robust: 95 tests, 130 stress questions, data quality filtering, API retry logic
Reproducible: pip install, set API key, ingest (~3 min), ask questions
Clean, minimal, readable code | No LangChain, no framework bloat